## Slide 1: pfs.ipmu.jp internal design
Atsushi Shimono
(on behalf of admin team)
as of 2016/10/02
PFS IPMU internal note– PFS-IPMU-00001-008

## Slide 2: ToC
Overall network diagram, physical distribution
Administrative resources
Hardware computing resources
VM management
External service organization
Internal operational service organization
Service startup procedure
PFS Simulators
Service for IPMU internal

## Slide 3: Overall network diagram
All on PFS internal LAN
External interfaces
  To global
    pfs.ipmu.jp : VM
    pfspipe.ipmu.jp : VM
  To IPMU internal
    pfscalc : NFS and samba storage service
Internal services
  Static lease based DHCP server (mgmt-dhcp) : testing on-site ICS
  RAID1 storages (pfsdisk) : 3TB x 3
    Server storage, virt disk store, simulator storage
    Weekly disk health verify, 2 hotswap disk
  LDAP server (pfs.ipmu.jp)
  Most of physical server is just VM host server
    Except for pfsdisk (NFS storage), pfscalc (IPMU internal services)

## Slide 4: Overall network diagram
global
IPMU internal
internal
pfscalc
2,
4LP
(samba)
pfsdisk
2,
8LP
extVM2
4,
noRAID
VM
server + simulator VM hosts
r410-1
dl360-2
4, HT
VM-win

## Slide 5: network
Ethernet connection for internal LAN is moving to managed L2 switches. For networks to IPMU and global, using (and will use) non-managed L2 switch.
Servers
  internal: Cisco 2960C (8+2SFP)
  IPMU-LAN: Dell PC5424
Simulator rack
  Fujitsu 24port 1G for master
  Cisco 2950 48port 100M for low speed hosts

## Slide 6: Place of physical host
At wall side (server system) – from corner
  CAD PC
  pfsdisk : storage for services
  pfscalc : storage for internal use
  extVM2 : host for external service VMs (port to global has no IP address)
  R410-1 (on desk): host for external service VMs
At work desk (simulator services)

## Slide 7: Administrative resources
PFS internal wiki
  https://pfs.ipmu.jp/wiki/System : track on-going status
Munin status panels
  https://pfs.ipmu.jp/munin/index.html
  http://himor.in/munin-cgi/ipmu.jp/index.html (backup)
libvirt VM panel (TBD)
mail lists
  Admin : pfs@pfs.ipmu.jp
  Munin warnings : munin@pfs.ipmu.jp

## Slide 8: Hardware computing resources
Base configs: https://pfs.ipmu.jp/wiki/System/install/linux-base
Bridges for physical ethernet ports (to make virt live migration possible)
br0 : PFS-LAN
br1 : external
br2 : IPMU internal
Hosts
see lists at https://pfs.ipmu.jp/wiki/System/hardware
External server (br0 to PFS-LAN, br1 to external) - run only VMs requires global address
  extvm2 (.5) Corei5 4570 3.2G 4core noHT 16G (new config)
Internal server (br0 to PFS-LAN, br2 to IPMU) - run only VMs requires IPMU network
  r410-1 – external services
  dl360-2 – Windows VMs
Service hosts
  pfsdisk (.3) C2D 2.6G 2core noHT 3G
  pfscalc (.4) Xeon 2.66G 2core noHT 2G

## Slide 9: VM management
Virt disk storage on NFS
  /virt: at pfsdisk (RAID1 3TB)
  /virt-win: at dl360-2 (RAID1 1TB) – for Windows VMs
    Mostly used at host local
Local storage only for host operation
VM operation via virsh interface
  Remote monitoring via libvirt feature under testing
VM hosts could be easily replaced
  No configuration difference among hosts, except for network bridge (existence of bridges to IPMU or global)

## Slide 10: External service management
Both pfs(srv) and pfspipe is on VM, rely on external services from VMs
Storage for server services at pfsdisk:/server
  admin: administrative files (incl. backup)
  archive: archive of download or old data
  backup: backup of ldap, mysql, pgsql
  home: to be mounted as /home
  httpd: web storage
    http-*, https-* : mostly mounted as web
  services: storage for services
    gitolite
    jira, jira-pipe
    mailman
    munin
    mysql, postgresql
  storage: to be open as https://pfs.ipmu.jp/*
    dd-images, ms-vl, etc.
  subversion: subversion repositories

## Slide 11: Internal operational service management
Mgmt-dhcp (.1)
  dnsmasq (dhcp)
mgmt (.7)
  Munin for external view
pfsdisk (.3)
  RAID 1 storage server (3TB x3, 1S)
    /server : external server data, /home
    /virt : VM images
    /simdata : data storage for simulators
pfscalc3 (.6)
  RAID 1 storage for /virt-win, Windows VM host
landfill (.32)
  landfill services
.db2 (.37; jessie)
  Pgsql, mysql database service
  Daily backup for every databases

## Slide 12: System startup procedure
Power on, wait for startup of network switch
Power on pfsdisk, system health check (KVM)
Power on extvm2, system health check (KVM)
Power on mgmt-dhcp, pfssrv, pfspipe on extvm2
  Check services (apache, mailman) on pfssrv
Restart ntp service on pfsdisk, extvm2
Check LDAP loading on pfsdisk (LDAP server = pfssrv)
Power on pfscalc, check eth are up
Power on VM host servers (no order)
Bootup service VMs (mostly no order)
  Services rely on DB will resume their connection on db startedup

## Slide 13: PFS Simulators
~100TB RAID6 iSCSI storage server (10.100.200.170-179)
  iSCSI device multipath : 10.100.200.170-177
  Server admin IF : 10.100.200.178-179
Axis PTZ surveillance camera (10.100.200.180)
Cisco switch
  Cs (8port) : 10.100.200.190
  CB2F (24port x2 FlexStack) : 10.100.200.191-192
  SpS (24port) : 10.100.200.193
  CB2F E-LAN (8port) : 10.100.200.194
  C48a (48port; 100BASE): 10.100.200.195
  F24a (24port; 1G): 10.100.200.196
  p5424a (24port; 1G): IPMU-LAN, 192.168.156.29
KVM
  Simulator rack : 10.100.200.203, 192.168.156.33
  Servers : 10.100.200.212, 192.168.156.32
PDU
  Simulator rack : 10.100.200.204
  Servers : 10.100.200.211

## Slide 14: Service for IPMU internal
Shared storage service
  hosts
    192.168.156.70 (10.100.200.4) in service (RAID1 4TB, 6TB)
  NFS, Samba : currently 4TB
    Access: 192.168.156.70:/data1
    Samba user/pass: set at host by smbpasswd
  Storage for backup (via rsync etc.) : 3TB
    “rsync” to 192.168.156.70:/data2
    e.g. “rsync -a --delete --link-dest=<priv> <orig> <backup>”
VM service
  Use VM hosts for simulators
Bots
  Dropbox (cit) running at jessie.pfs.ipmu.jp (by account: atsushi.shimono)
    Syncing to 192.168.156.70:/data1/cit-dropbox/Dropbox
    Check status via “dropbox status”

## Slide 15: Nearby ToDo
Reorganize munin services
  Telemetry archive for all hosts and services at mgmt2
  Warning email service at mgmt-dhcp, restricted “always up” infrastructures
Redundant physical host
  Prepare backup for r410-1