## Slide 1: Requirements on on-site DRP
Atsushi Shimono (IPMU)
2015/09/11
PFS Software team Study Note : SSN-00015-001+

## Slide 2: Outline
This note summarizes current understandings on requirements for on-site DRP package of both 1D and 2D. On-site DRP package is supposed to be a subset of (full) DRP package, but has some special requirements for on-site quick data quality assurance work (QA).
Background
Requirements and assumptions
  On entire on-site DRP
  On 2D DRP
  On 1D DRP
  From specific observation (survey) modes
Backend and user interface

## Slide 3: Background
PFS will be used in various aspects, such as for survey observations, and as a facility instrument of Subaru for PI-type observations and queue mode observations. Especially for survey and queue mode, data quality assurance right after each exposure is quite important for using observation time efficiently.
Full DRP package could also be used for on-site quick data reduction, but full DRP is assumed to take huge computing resource for its processing and is not the case. So, PFS project needs to deliver on-site DRP package as a subset of full DRP package with a special configuration and some additional interfaces.
This note describes
Requirements on on-site DRP from operational point of view
Requirements for 1D/2D on software design point of view
External interface including user interfaces

## Slide 4: Requirements and assumptions – entire on-site DRP
Analysis need to be finished within next exposure
  Will be around 6min or so
    Assumed shortest science exposure as 7.5min (cosmology survey)
    Need to allocate on data transfer as 1min
  After end of next exposure, next data will arrive
  No need to analyze calibration data
  If we will not go aggressive, can eat another 1min of data transfer
    Results of QA is not required for next exposure, we can continue until next data arrives
Results will be used only for on-site data QA
  No need to determine object type etc.
    Or can use pre-defined object type for processing, even.
  Sky emission subtraction is TBD
    PSFs will not be measured on the data itself
    Can measure sky level with “sky” fibers? (TBD for IR range)
  (TBD) Check statistics only for lines/continuum/absorption above certain S/N?
  (At least) Need to check and output results from calibration targets marked in data
    Sky fibers, with no light source (determined by imaging data)
    Calibration fibers, with F-type star (both primary and secondary?)

## Slide 5: Requirements and assumptions – 2D DRP
Since most of processing time of DRP is assumed to be in 2D, which “heavy” component to reduce from 2D DRP for on-site DRP will be a good question to us. We also are possible to learn from quality of QA compared with options, from HSC 2D on-site processing or test analysis.
Components need to be switched off in some way (flag or configuration)
  Especially for components which will not change formats
    e.g. input and output format is the same
    Or say, components like 2D image to set of 1D spectra cannot be removed from pipeline
Configuration parameters need to be switched to pre-measured data
  e.g. flat image, PSF mapping parameters over image
  If load is quite heavy, we need to fix parameters even changes are not small
    Of course, depends on their effect, but….
    Need to think about pre-measured map of parameters (e.g. PSF for FRD)
Will not use up-ramp raw data, but use only pre-processed data at summit
  Even if 2D DRP will switch to use (entire?) up-ramp data, on-site will only process final one
    To save time… (resultant S/N will not so change with fine modeling of PSFs)
  Also data transfer will take time rather than pre-processed data
    On-site DRP can start earlier for NCU data – for only with pre-processed data
Misc
  Pixels with sky emission need to be masked or removed for 1D processing
  Roughly estimated noise spectrum need to be supplied for S/N estimation in 1D

## Slide 6: Requirements and assumptions – 1D DRP
Since aim of this on-site DRP is just for data QA, we do not need to measure detailed characteristics or statistics of targets, such as redshift, lambda and width of every lines, or line identifications – but depends on target category.
On-site DRP does not access to previous exposures with the same configuration
  No need to combine supplied spectrum with others
Survey will not measure redshift with a single exposure
  Also redshift measurement success rate is not a target of QA
  No need to process template matching
For pixels with S/N higher than certain value (TBC) need to be measured for statistics
  Wavelength and width (TBC)
  Again, no need to match with template, but just for individual lines
Need to check quality of targets marked as sky and calibration star
  If a sky target has higher level from certain range, condition was bad
  If a calibration star has different statistics than expected, something wrong
    Field acquisition, AG, target assignment, etc…
  Need to check every targets, to match with specified in FITS or attached data
Misc
  2D pipeline will provide noise spectrum as the same as full DRP, but not in the same quality
    But just use it.

## Slide 7: Requirements and assumptions – from specific modes
On-site DRP will have specific requirements from each survey modes – cosmology, galaxy, and GA. Also these (or sub-groups of these?) could also be used from non-survey observations, but details are not discussed yet, e.g. flag per target or exposure?
(NEED TO GATHER FURTHER INFORMATION FROM SURVEYS)
Cosmology
Galaxy (AGN)
GA

## Slide 8: External interfaces
On-site DRP will be hosted at Hilo
Data and command (invoke) input
  Data interface is push from Subaru (Gen2)
    Will be into specific storage space, such as NFS
    Will be the same as HSC on-site DRP
  Assuming no direct interface from ICS (TBD)
    Need to study how HSC on-site DRP is invoked
    No automatic update of exposure configuration at a night (TBC)
User interface will be in other package?
  Results will be added into exposure configuration database
    How to attach to archived data is TBD!
  For operation at summit, check via status UI for exposure database
  For queue mode, PFS will discuss with Subaru how to insert into their one
    But not automatic, operator need to check before input to queue dispatcher